## Slide 1
Programming With Python (202044504)
Autonomous Navigation System
Path Planning & Obstacle Avoidance
Presented by:
Riya Patel (12402120601067)
Nataansh Kayasth (12402120601054)

## Slide 2
Introduction & Objective
Objective
Develop an AI-based path planning and obstacle avoidance system for autonomous robots or simulated environments using Python.
Problem
Robots need to navigate environments autonomously — reaching goals while avoiding obstacles in real time.
Approach
Combine classical graph-search algorithms (A*, Dijkstra, RRT) with reinforcement learning for adaptive decisions.
Outcome
A simulated environment with visualised paths, performance metrics, and multiple scenario support.

## Slide 3
System Architecture Overview
Perception Layer
Sensor input · grid map generation
Localisation & Mapping
Position tracking · environment model
Path Planning Layer
A* / Dijkstra / RRT algorithms
Obstacle Avoidance
Dynamic re-routing · collision detection
Control Layer
Actuator commands · movement execution

## Slide 4
Path Planning: A* & Dijkstra
A* Algorithm
How it works
Uses heuristic function: f(n) = g(n) + h(n)
g(n) = cost from start to node n
h(n) = estimated cost to goal (heuristic)
Explores nodes with lowest f(n) first
Guarantees shortest path if h(n) is admissible
Uses priority queue (min-heap)
Dijkstra's Algorithm
How it works
Explores all paths uniformly: f(n) = g(n)
No heuristic — explores all directions
Guarantees optimal shortest path
Works on weighted and unweighted graphs
Higher time complexity than A* in large grids
Suitable for static environments
A* vs Dijkstra — A* is faster due to heuristic guidance; Dijkstra explores thoroughly but is simpler to implement.

## Slide 5
Path Planning: RRT (Rapidly-exploring Random Tree)
What is RRT?
RRT incrementally builds a tree by randomly sampling the configuration space and extending toward samples. Ideal for high-dimensional and continuous environments.
1
Initialise tree
Place root node at start position.
2
Random sample
Pick a random point in free space.
3
Find nearest
Locate nearest tree node to the sample.
4
Extend
Grow tree toward sample by step size Δ.
5
Collision check
Discard extension if it hits an obstacle.
6
Goal check
Stop when tree reaches goal region.
RRT Advantage: handles complex, high-dimensional spaces and non-convex obstacles better than grid-based methods.

## Slide 6
Obstacle Detection & Avoidance
Detection Methods
Grid-based sensing
Robot scans adjacent cells; obstacles flagged as blocked nodes in the occupancy grid.
Collision prediction
Trajectory simulated ahead in time; potential collisions identified before movement.
Bounding box check
Object extents compared against planned path segments.
Sensor simulation
Simulated LIDAR / proximity sensors return distance to nearest obstacle.
Avoidance Strategies
Static obstacle mapping
Pre-loaded obstacles marked on grid; planner routes around at planning time.
Dynamic re-routing
Path recalculated when new obstacles appear mid-navigation.
Potential field method
Obstacles create repulsive fields; goal creates attractive force on the robot.
RL-based avoidance
Agent learns avoidance behaviour through reward/penalty feedback over episodes.

## Slide 7
Reinforcement Learning for Decision Making
Environment
Grid world / physics
State
Robot pos, obstacles
Agent
RL policy network
Action
Move / rotate / stop
Reward
+1 goal, -1 collision
↻ Feedback loop: reward signal updates policy via Q-learning / Deep Q-Network (DQN)
Q-Learning
Off-policy TD algorithm. Learns Q(s,a) = expected future reward for action a in state s.
Reward shaping
+10 goal reached · −10 collision · −0.1 per step (encourages shorter paths).
Exploration
ε-greedy policy: explore randomly with probability ε, exploit best known action otherwise.
Convergence
After sufficient episodes, agent learns optimal policy for static and dynamic environments.

## Slide 8
Simulation Environment & Visualisation
Grid simulation (PyGame)
Start
Goal
Path
Obstacle
Tools & Features
PyGame renderer
Real-time grid display, robot movement, path overlay
NumPy grid
Efficient occupancy matrix for obstacle and path data
Multiple scenarios
Open field, maze, dynamic obstacles, crowded space
Algorithm selector
Switch between A*, Dijkstra, RRT at runtime
Performance HUD
Path length, steps, time elapsed shown on screen

## Slide 9
Performance Metrics & Deliverables
Path
Length
nodes traversed
Execution
Time
milliseconds
Collision
Rate
% avoidance success
Episodes
to Learn
RL convergence
Algorithm Comparison
Algorithm | Optimal? | Speed | Use case
A* | Yes (admissible h) | Fast | Static grid
Dijkstra | Yes | Moderate | Weighted graphs
RRT | Probabilistic | Fast for high-D | Continuous space
RL Agent | Learned policy | Real-time | Dynamic obstacles
Autonomous Navigation System · ADIT

## Slide 10
Thank You
Project: Autonomous Navigation System Course: Programming with Python (202044504)